## Slide 1: Multimedia Systems
Dr Laura Toni
l.toni@ucl.ac.uk
University College London

## Slide 2: Today Lecture
Introduction to Information compression
  Source Coding
  Information and Entropy
  Variable length coding
  Quantization
Multimedia Systems
  Image and Lossy Compression
    Transforms
    JPEG Quantization
    JPEG Lossless Compression
  Video Compression
    Motion Compensation

## Slide 3
Source Encoding
Source Coding
Lossless
(text, programs)
Lossy
(images, videos)
Incremental Encoding
Huffman Code
Run Length Encoding
Notes: Two main coding types are used in Mobile Communications
Speech Coding – source coding
  Reduces the redundancy to minimise the bandwidth
Error Coding – Channel Coding Techniques
  Increase the redundancy to reduce errors and improve reliability

## Slide 4
Source Encoding
Lossless
Lossy
Shannon’s first theorem (1948)
Expected code length relates to the source entropy
R
D
Source recovered with a distortion D (function of the coding rate)
Speech and Video coding
Source Coding
Notes: Two main coding types are used in Mobile Communications
Speech Coding – source coding
  Reduces the redundancy to minimise the bandwidth
Error Coding – Channel Coding Techniques
  Increase the redundancy to reduce errors and improve reliability

## Slide 5: Why do we compress?
These are related to the 3 types of redundancy in images/videos:
  Interpixel redundancy
  Psychovisual redundancy
  Coding redundancy

## Slide 6: Coding Redundancy
Some colors are more common than others
For example, black, brown, and red hardly appear in this picture
This is sometimes called coding redundancy

## Slide 7: Interpixel Redundancy
Blue pixels tend to occur next to other blue pixels; yellow pixels are near other yellow pixels
This spatial correlation is sometimes called interpixel redundancy
There are also interspectral and interframe redundancy

## Slide 8: Psychovisual Redundancy
Some parts of the scene are very homogeneous (sky)
Other parts are very busy (flowers) and could hide noise
This is sometimes called psychovisual redundancy

## Slide 9: Why Lossy?
We can get away with lossy compression because your eye doesn’t see everything anyway
  Contrast sensitivity function
  Mach bands
  Spatial masking
  Oblique effect
Human Visual System Issues

## Slide 10: Spatial Masking
A stimulus is harder to see in the presence of large visible spatial and temporal changes in luminance
Line presented near a luminance edge is harder to see as it gets closer

## Slide 11: Spatial Masking
Implication: Can allow more error in busy parts of the picture

## Slide 12: How well is the compression doing?
We would like to have a low bit rate and yet a high image/video quality
(there are also other factors – not covered today- such as complexity, error resilience, delay etc. )
If you use lossy compression, need to be able to measure the quality

## Slide 13: MSE Metric
The most common computable measures are the MSE
where F is the input image, G is the output image, and the images are of size N by M

## Slide 14: PSNR Metric
The MSE is often reported in logarithmic form as a signal-to-noise ratio:
where D0 is a normalization factor
  Do often chosen to be the square of the maximum possible input value (e.g., 2552)
  Then it’s called a “peak SNR” or PSNR

## Slide 15: JPEG Example

## Slide 16: Thank You