## Slide 1: Multimedia Systems
Dr Laura Toni
l.toni@ucl.ac.uk
University College London

## Slide 2: Today Lecture
Introduction to Information compression
  Source Coding
  Information and Entropy
  Variable length coding
  Quantization
Multimedia Systems
  Image and Lossy Compression
    Transforms
    JPEG Quantization
    JPEG Lossless Compression
  Video Compression
    Motion Compensation

## Slide 3: Block Diagram for Image Compression
Signal Decomposition:
  Compact energy into a small number of coefficients
  Decorrelate the components of the signal
Quantization:
  Make approximations to the transform coefficients
  Selectively throw away information
Lossless coding
  Variable length coding (e.g., Huffman Coding)
  Choose short/long codewords to minimize number of bits

## Slide 4: Transform Coding
We are interested in transforming a signal or image from the spatial domain to the frequency domain
by itself, the transform – does not save any bits – does not introduce any distortion
both of these happen when we throw away information - “lossy compression” implemented by the quantizer
A
x
u
A-1
u
x

## Slide 5: 2-d DCT Basis Functions
The whole array of
basis functions looks
like this:
The array of DCT
coefficients tells how
much of each of these
basis images we need
to regenerate original image
Low frequencies
High
frequencies
DC coefficient

## Slide 6: Why is the DCT a good idea?
DCT has excellent energy compaction for highly correlated data (smooth areas).
Low frequencies in the DCT correspond to smooth areas
We can quantize less heavily low frequencies
Smooth areas in the images have pixels highly correlated
Pixels around edges are less correlated
Our visual system is less sensitive to distortion around edges
We want to protect smooth areas the most

## Slide 7: Quantization after Transforming
After the DCT, we still have N2 numbers to represent a block:
N2 pixels ↔ N2 coefficients
However, the N2 coefficients will have
  Lot of values near zero
  Lot of values which represent high frequency info

## Slide 8: Block Diagram for Image Compression
Signal Decomposition:
  Compact energy into a small number of coefficients
  Decorrelate the components of the signal
Quantization:
  Make approximations to the transform coefficients
  Selectively throw away information
Lossless coding
  Variable length coding (e.g., Huffman Coding)
  Choose short/long codewords to minimize number of bits

## Slide 9: Let’s continue the example
Pixel intensity (N2 values)
DCT
Transformed coordinates
(N2 values)
How can we apply the quantizer?
source
DCT

## Slide 10: Let’s continue the example
We consider a quantizer matrix, in which higher frequency are quantized more heavily
Low frequencies
High
frequencies

## Slide 11: Let’s continue the example
DCT
Quantizer
source
DCT
Quantized DCT
Q matrix

## Slide 12: Can we reconstruct the image?
however visually the blocks are not very different
Hence, we highly compressed the image without having “perceptual” losses!

## Slide 13
Source Encoding
Source Coding
Lossless
(text, programs)
Lossy
(images, videos)
Incremental Encoding
Huffman Code
Run Length Encoding
Wavelet Compressor
Vector Quantization
Transform Coding
Notes: Two main coding types are used in Mobile Communications
Speech Coding – source coding
  Reduces the redundancy to minimise the bandwidth
Error Coding – Channel Coding Techniques
  Increase the redundancy to reduce errors and improve reliability

## Slide 14
Take Home Message
Information theory tells us to look at the probability of the source when coding (most probable words, shortest bits)
Quantizer follows the same concept: quantize heavily the least probable ranges
Image compression is composed of
  There is redundancy in the images.
  Artefacts in high-frequencies (edges) are less noticeable from the human eye
  Source transformation (to compact the energy – most high frequency values will be low)
  Quantizer (2D quantizer that will cut off high-frequencies)
  Zig-zag rastering will maximize the probability of having 0s
  Huffman lossless code as last step
Notes: Two main coding types are used in Mobile Communications
Speech Coding – source coding
  Reduces the redundancy to minimise the bandwidth
Error Coding – Channel Coding Techniques
  Increase the redundancy to reduce errors and improve reliability

## Slide 15: Thank You