## Slide 1: PCM Systems
Dr John Mitchell University College London
j.mitchel@ee.ucl.ac.uk

## Slide 2: Sample and Hold
m(t)
Notes: The job of a Sample and Hold is to memorise the input voltage on command of a clock signal.

## Slide 3: Sampling - the time domain
PAM signal
m(t)
Message m(t) with spectrum M(f); M(f)=0 for |f|>W
Sampling pulse train
T
Notes: This slide shows some of the corresponding time-domain waveforms. The input signal waveform m(t) is multiplied by the sampling pulse train xp(t) to produce a pulse amplitude modulated (PAM) signal. This process is sometimes referred to as natural sampling since the amplitudes of the pulses follow the amplitude of the sampled message signal within each pulse.

## Slide 4: Sampling - the frequency domain
Lowpass filter response
0
1/T
2/T
f
-1/T
-2/T
fm
-fm
f
M(f)
0
1/T
2/T
f
-1/T
-2/T
Notes: This slide shows the situation in the frequency domain. The original message m(t) with spectrum M(f) is bandlimited to |f|<W. this is sampled at rate Fs=1/T<2W. the resultant sampled signal, spectrum contains replications throughout frequency space of the original signal spectrum, separated one from another by Fs and scaled in amplitude depending upon the spectrum of the sampling pulse waveform.

## Slide 5
Sampling – Frequency Domain
If we redraw the figure showing frequency we see that we can calculate the frequency spacing of each of the copies of the original spectrum.
0
f
-fs
fs
-2fs
2fs
fs-fm
-fs+fm
fm
fm
fs+fm
-fs-fm
2fs+fm
2fs+fm
Notes: If we use a higher sampling rate then the centres of the DSB-SC spectra will be further apart and the spectrum of the sampled waveform will appear as in Fig. 10.4.
In this case a guard band appears between the repeated spectra. This is the practical situation because it is impossible to construct an ideal filter. All we need now is a filter which passes everything up to fM and then starts to attenuate. Provided the attenuation is sufficiently large at fs - fM the signal will be recovered virtually undistorted. A typical application is telephone bandwidth speech which is band limited to 3.4 kHz but is usually has a sample rate of at least 8 kHz. The guard band is then 8.0 -2(3.4) kHz = 1.2 kHz
Fig. 10.4 Spectrum of sampled analogue signal with

## Slide 6: Aliasing - frequency domain
0
1/T
2/T
f
-1/T
-2/T
Region of spectral overlap
Notes: This slide illustrates aliasing. This occurs if Fs<2W. The result is that the various replications of the signal spectrum, centred upon multiples of Fs, overlap with one another. In the overlap region it is not possible to distinguish between frequency components in m(t) which are slightly less than Fs/2 and those slightly greater than Fs/2, the latter masquerading - or operating under an alias - as components within the lower frequency range. The result is distortion in the upper frequencies of the signal spectrum.
The Nyquist sampling theorem
From the foregoing we have intuitively proved Nyquist’s Sampling Theorem which states that the sampled signal can only be reconstructed provided the sampling rate, fs≥ 2fM where fs=1/Ts. The minimum value of fs is known as the Nyquist rate.
Consider the case of a single sinusoid of frequency fM All the signal energy is concentrated precisely at the cut-off frequency of the filter so there is clearly an ambiguity as to whether the signal is inside or outside the passband of the filter. To resolve this ambiguity we must choose fs > 2fM. We can see the justification of this statement by assuming that we take a sample of the sinusoid at the instant it crosses zero. If fs= 2fM then successive samples will also be taken as the waveform crosses zero - not a very useful situation!
Always make fs > 2fM.

## Slide 7: Quantisation
VL
VH
M=5
V01
V12
V23
V34
m0
m1
m2
m3
m4
m0
m0
m1
m2
m1
m2
m4
m3
m2

## Slide 8: Quantisation
Allow signal to assume only specific values from some finite set
May be uniformly spaced levels - or may be deliberately non-uniform
Uniform quantisation results in an error bounded by one half of a quantel step (±D/2 - resulting ‘quantisation noise’ (or distortion) has approximately uniform distribution with variance D2/12)
Quantisation is followed by encoding, each level being represented by a codeword (e.g. 8 bits)
Notes: Quantisation involves restricting a signal to certain discrete amplitude values or levels. With uniform quantisation these levels are equally spaced one from another, although non-uniform spacing is also employed and can give improved performance so far as the resulting mean square quantisation distortion (power) is concerned.
With uniform quantisation – and assuming the signal stays within the finite range of the quantiser – the error is always within D/2, with D the separation between levels. Since the quantisation error waveform is essentially composed of approximately triangular segments the quantisation error power corresponds to the power in a triangular waveform of amplitude D/2. This is readily shown to be D2/12. For non-uniform quantisation the optimum quantising characteristic depends upon the signal amplitude distribution
In PCM the quantisation process is followed by encoding, with each level represented by a codeword. For PCM telephone 8 bits per level are commonly employed

## Slide 9: Quantisation
We assume that the input has a minimum allowed value of VL and a maximum allowed value of VH. We will divide this range of values into M possible values.
Therefore each division will cover
Where  is the step size
Notes: We assume the signal, mq(t) always lies in the range VL to VH which is divided into M equal intervals each of size .  is called the step size and is given by
In practice it is usually an even number and a power of 2 (e.g.23=8). In the centre of each step is located the quantisation level, m0, m1, m2, etc. The quantised signal, mq(t) is generated according to the following rules. If m(t) is in the range 0, mq(t) maintains the constant level m0. If m(t) is in the range 1, mq(t) maintains the constant level m1 and so on through each step. The change from, for instance, m0 to m1 is abrupt as the signal passes through the transition level L01 etc. The quantised signal can only take on one of the discrete levels and always takes on the one closest to the value of m(t). When the value of m(t) lies on a transition level it does not matter which quantisation level is adopted but in practice the signal is statistically unlikely to exist exactly on a transition level anyway. Although the quantisation levels are separated by , m(t) is never more than /2 away from a quantisation level so at every instant the quantisation error is given by,
The quality of the approximation can be improved by using smaller step sizes so increasing the number of allowable levels. The number of levels required depends on the application and the sensitivity of the recipient of the quantised signal to the quantisation error. 256 levels (28) is adequate for good quality commercial colour television. The picture quality will be considerably less acceptable with 64 levels (26).

## Slide 10: Quantisation Noise
001
000
010
110
111
101
Quantisation noise
Signal sampling instants
Binary code for mQ(t) at sampling instants
Binary pulse
sequence
Notes: As mentioned previously the process of quantisation introduces distortion – quantisation distortion – generally termed quantisation noise since it is noise like in character. We will let Q(t) denote this quantisation distortion waveform. It is a bounded signal lying in the range D/2. Notice that most portions of Q(t) are approximately linear – giving triangular waveform segments – and this applies to an even greater extent for finer quantisation using most quantisation levels. Hence the quantisation noise power – or mean square value – may be determined as closely approximating the power in a triangular wave of amplitude D/2. Equivalently, we may note that Q(t) has a approximately uniform probability density function fQ(v), of density 1/D over the range D/2. The variance of this distribution is D2/12 corresponding to the mean square value of the process – or the quantising noise power.
Note that Q(t) contains frequent ‘sharp’ transitions and so extends over a wide frequency range. The sampling process associated with PCM means the Q(t) is effectively sampled as well as m(t). The sampling rate is set to ensure that m(t) does not suffer undue aliasing – but this does not apply to the much wider band waveform Q(t)

## Slide 11: Pulse Code Modulation

## Slide 12: Companding
With uniform quantisation signal level variations (e.g. between different ‘talkers’) give rise to variation in the signal to noise ratio
Compression prior to quantisation reduces the range of variation, compensating re-expansion is applied at the receiver
A logarithmic characteristic gives a nominally uniform SNR
Notes: The quantisation process discussed so far uses a uniform separation between quantisation levels. Provided the signal always exhibits the maximum excursion this is adequate. However, if there is a very wide signal dynamic range (difference in dB between the expected maximum and minimum signal levels) then low level signals will exhibit a relatively poor signal-to-quantisation noise ratio.
The signal is close to zero and all the fine detail is lost due to quantisation, only a small number of codes are being transmitted. For large signal levels this loss of detail is relatively unimportant so coarse quantisation is acceptable. Also, at low signal levels our assumption that the signal has a uniform probability density function in each quantisation level is no longer valid.
We can overcome this problem by a technique known as companding (derived from compressing and expanding) in which the quantisation levels are non-linearly spaced, being closer together (compressed) for low level signals and further apart for high level signals. Obviously, the receiver must apply the reverse process (expanding) or the decoded signal will be distorted. Using companding the precision with which the analogue signal can be constructed is more or less constant regardless of its amplitude.

## Slide 13: Companding & quantisation
Analogue
input
signal
1001
0
Signal
Companded quantised signal
1111
1110
1101
1011
1010
Binary code
1100
1000
t
Compress
Quantise
Encode
Digitised
output
signal

Sampling
In practise compression implemented digitally, operating on a signal quantised to high accuracy
Notes: Rather than have a non-uniform A/D converter we pass the analogue signal through a compressor and then pass the compressed signal to a uniform A/D converter. There are two main types of compression laws which we will look at in the next slides.

## Slide 14: Logarithmic Companding - continued
The Logarithm function, f(x) takes negative values for x<1
The A-law companding arrangement adopted by ITU/CCITT makes use of a linear segment for small amplitudes and a logarithmic segment for large amplitudes
The resultant characteristic provides logarithmic compression for large amplitude signals
Log function
A-Law Compression Characteristic
Input
Output
Notes: There are two main compression laws. The µ -law which is used in the USA and the A-law used in the UK and the rest of Europe.
NOTE: There is no need to remember these formulae.

## Slide 15: Logarithmic Companding - continued
The Logarithm function, f(x) takes negative values for x<1
To overcome this the m-law, adopted in North America, involves shifting the function as shown, equivalent to employing f(x-1)
The resultant characteristic provides approximately logarithmic compression
For negative input values the function is reflected through the origin
Log function
-Law Compression Characteristic
Input
Output

## Slide 16: Logarithmic Companding - continued
To accommodate negative input signals the A-law or m-law characteristics are reflected through the origin
Input
Output
-Law
A-Law

## Slide 17: PCM in Telecommunications
Nominal 4 kHz speech signal
8 kHz sample rate
8 bits per sample
64 kbit/s for a single telephone speech channel
Multiplex 30 such speech signals (synchronous word interleaving) - together with further two 64 kbit/s signals used for signalling and control - to realise a 30 channel PCM system signal at approximately 2 Mbit/s (more precisely, 2048 kbit/s)
US variant is 24 channels, originally with least significant bit ‘stealing’ one frame in 6 to provide for signalling but since this only provides a 56 kbit/s ‘clear channel’ for data now moved to 23 channels plus one reserved for signalling
Notes: The internationally agreed and standardised arrangement for PCM telephony stems from these early proposals. For PCM telephony a telephone signal is 3dB bandlimited to 300Hz to 3400Hz and is though of as nominally a 4kHz channel. From sampling theory this implies a sampling frequency of not less that 8kHz. In fact as we know the channel does not actually extend to 4kHz we use 8kHz as the sampling frequency. Quantised samples are represented with 8 bit resolution (256 levels) so that a sampled, quantised and pulse encoded PCM signal for telephony is 64 kbit/s
PCM signals can also be time division multiplexed. PCM telephony involves conveying together many similar channels over the same medium. One such system is the T1 digital system, shown in Fig. 11.13, where a number of analogue speech signals can be accommodated in a single channel. The first level in the multiplexing hierarchy involves combining 30 speech signals together with signalling and control data in to a 32 x 64 kbit/s = 2.048 Mbit/s stream on a byte interleaved basis.
In the US only 7 bits are used given a rate of 56 kbit/s and they also use a different multiplexing structure with 24 speech signals being combined into a 1.544 Mbit/s stream.

## Slide 18: PCM frame structure
Primary multiplex rate = 32 x 64 kbit/s = 2.048 Mbit/s, channels are word (byte) interleaved
30 channels for speech, 2 for signalling and control
Slot 0 is for synchronisations (framing)
Slot 16 is for signalling
Slots 1-15 and 17-31 carry PCM speech
0
16
1 - 15
17 - 31
125 s
Notes: At the first level of the multiplexing hierachy 30 digitised speech signals – each represented by a 64 kbit/s binary data stream – are combined on a word interleaved basis into a frame structure comprising 32 8-bit words. In this frame time slots 1-15 and 17-32 carry digitised speech samples while time slots 0 and 16 are used to convey signalling and control data. The aggregate data rate for this primary level multiplexed signal is 2048 kbit/s or 2.048 Mbit/s, commonly referred to informally as a 2 Mbit signal.

## Slide 19: Bit interleaved multiplexing
x 4
Time
division
multiplexer
1
0
0
0
0
1
Input rate Fi bit/s/channel
Output rate Fo
= 4 x Fi bit/s
m1
m2
m3
m4
Output bit sequence derived from input tributaries: m1,m2,m3,m4,m1,m2,m3,m4
1
1
1
0
1
0
1
0
1
1
Notes: We can go a stage further and multiplex the multiplexed PCM signals using a hierarchy of multiplexers as shown in Fig. 11.15. We start with a basic E1 signal with a bit rate of 2.048 MBs-1 comprising of 32 channels (30 voice, 20 signalling). Four E1 lines are multiplexed in a multiplexer to generate an E2 transmission system. Four of these E2 lines are multiplexed in to produce an E3 transmission system and an E4 system is generated by multiplexing four E3 lines. Additional frame synchronising bits are required at each stage. Even with very stable clock generators at each PCM source the signals into the level 1 multiplexer will be asynchronous and “bit stuffing” may be necessary to keep all the PCM signals synchronised. The receiver must, of course, be able to identify the extra bits and remove them.
To generate the level one frame of 32, 64kbits-1 a technique called word-interleacing is used. In this technique 8 bits of each signal are taken together to form the frame. At multiplex levels above this (levels 2,3 and 4), bit-interleaving is used. This takes just one bit at a time from each of the 4 level 1 streams to form the higher level stream.

## Slide 20: Higher Order Multiplexing
Aggregate signal streams from several 30 channel systems for transmission on a single digital transmission bearer
Time division multiplexing - nominal factor of 4 at each stage
To allow for non-synchronous (plesiochronous) operation bit stuffing is used and the rate incease factor is > 4
Approximate rates are 2Mbit/s, 8 Mbit/s, 34 Mbit/s, 140 Mbit/s (Highest standardised rate, dates from early 1970’s; proprietary higher rate systems were developed)
Notes: Higher levels of multiplexing are used further to improve the utilisation of transmission facilities. The established multiplexing system is plesiochronous in that the various signal streams are combined in such a way that they form a single composite stream even though they may be derived from different equipment, with different clock oscillators operating a nominally the same bit rate (they are nearly isochronous). This multiplexing arrangement is now commonly reference as the plesiochronous digital hierarchy (PDH) to distinguish from the more recently introduced synchronous digital hierarchy which we will cover in the next section.
With PDH the higher rate signals are formed by multiplexing on a bit level in multiples of 4. Since the tributaries are not synchronous the multiplexers must allow for speed variations and so the outgoing rate must be at least 4 times the maximum tributary rate rather than 4 times nominal. Inevitably, this means that the output tends generally to outstrip the sum of the input streams. Under these conditions ‘bit stuffing’ - insertion of a non-data bit in the output stream – is employed to maintain the integrity of the output signal. These ‘stuffed’ bits must be removed at the demultiplexer and add considerably to the complexity of the signal format. In addition some information must be included in the outgoing data sequence to allow for synchronisation of the demultiplexer, which further increases the output data rate requirement. The result is an output rate that is rather more than 4 times the rate of the individual tributaries.

## Slide 21: Plesiochronous digital hierarchy (PDH)
1
30
30 PCM
speech signals
1st level
multiplexer
2nd level
multiplexer
3rd level
multiplexer
4th level
multiplexer
1
2
3
4
1
2
3
4
1
2
3
4
139.26
Mbit/s
2.048Mbit/s
8.448Mbit/s
34.368Mbit/s
Notes: The 2nd level multiplexer takes 4, level 1 streams each at 2.048 Mb s-1, often referred to as a 2MB signal and multiplexes them together to form a level 2 signal, which we see from figure 11.14 has a bit rate of 8.448 Mb s-1. However if we consider the bit rate of the data provided to this multiplexer we will see that the rate should be:
4 x 32 x 64kb s-1 =8.192 Mb s-1
This gives an extra 256 bits per second. These extra bits have two uses. Some of these bits are used to provide extra control information, while others are included because the bit rates of each of the 4 channels may not be exact. The 3rd level multiples has a raw bit rate of 4 x 8.448 Mb s-1 = 33.792 Mbs-1 and adds an extra 576 bits to give a 34.368 Mbs-1 signal which is often termed a 34Mbs-1 signal. The 4th level adds 1792 to 4 x 34.368 Mbs-1 = 137.472 Mbs-1 to give a total level 4 rate of 139.264 Mbs-1.

## Slide 22: PCM Multiplexing
 | AT&T |  | CCITT | 
 | Number of Inputs | Output Rate Mbit/s | Number of Inputs | Output Rate Mbit/s
First Level | 24 | 1.544 | 30 | 2.048
Second Level | 4 | 6.312 | 4 | 8.448
Third Level | 7 | 44.736 | 4 | 34.368
Fourth Level | 6 | 274.176 | 4 | 139.264
Notes: The 2nd level multiplexer takes 4, level 1 streams each at 2.048 Mb s-1, often referred to as a 2MB signal and multiplexes them together to form a level 2 signal, which we see from figure 11.14 has a bit rate of 8.448 Mb s-1. However if we consider the bit rate of the data provided to this multiplexer we will see that the rate should be:
4 x 32 x 64kb s-1 =8.192 Mb s-1
This gives an extra 256 bits per second. These extra bits have two uses. Some of these bits are used to provide extra control information, while others are included because the bit rates of each of the 4 channels may not be exact. If one of the signals is running
The 3rd level multiples has a raw bit rate of 4 x 8.448 Mb s-1 = 33.792 Mbs-1 and adds an extra 576 bits to give a 34.368 Mbs-1 signal which is often termed a 34Mbs-1 signal. The 4th level adds 1792 to 4 x 34.368 Mbs-1 = 137.472 Mbs-1 to give a total level 4 rate of 139.264 Mbs-1.

## Slide 23: Disadvantages of Plesiochronous Multiplexing
Complex signal structure
Difficult to obtain access to tributaries from the higher rate signals
Must climb up and down the ‘multiplexer mountain’ to add and drop channels (add-drop multiplexing) and to effect digital cross-connects
Little spare capacity for network control and management
Hence development of Synchronous Digital Hierarchy
Notes: These terms will be discussed in much greater detail when we look at SDH.

## Slide 24: Summary
Sampling Principles
Quantisation
Companding
PCM, DPCM, Delta Modulation
PCM in Telecommunications
PCM Frame structure
Plesiochronous digital hierarchy (PDH)