## Slide 1: Wireline Systems
Dr Cyril Renaud
c.renaud@ucl.ac.uk

## Slide 2: Overview
The ‘Copper’ Channel
  Twisted Pair
  Coax
Wireline Systems
  ISDN
  xDSL
  Ethernet
  DOCSIS
  Powerline Communications

## Slide 3: Twisted pair copper connections
The characteristics of the connection is very variable
Important characteristics include:
  attenuation
  phase response
  characteristic impedance
  crosstalk
  noise
Need an understanding of these in order to appreciate the limitations of the access network and how we may overcome some of these limitations

## Slide 4: Unshielded Twisted Pair UTP
Shielded Twisted Pair STP
Plastic Outer (Insulator)
Plastic Outer (Insulator)
Metallic Shield

## Slide 5: Attenuation
Attenuation is a function of frequency due to the “skin-effect”
Attenuation (dB/km)
Frequency (kHz)
1
1000
0.1
1.0
10
10
100
0.9 mm Cu
0.32 mm Cu

## Slide 6: Phase response
The phase response of twisted copper is fairly linear beyond about 10 kHz
At around 200 kHz, a cable contributes about 360º/km of phase offset
The variation between different cable diameters is very small
A non-linear phase response - corresponding to a non-flat group delay - would distort digital pulses

## Slide 7: Characteristic impedance
A twisted pair copper cable is a transmission line and exhibits behaviour just like any other transmission line
A wave travelling along the line sees an impedance
This is termed the characteristic impedance
1
10
100
Frequency (kHz)
Impedance (ohms)
0
400
800
1200
0.32 mm Cu
0.9 mm Cu

## Slide 8: Voice band modems
56 kbit/s over a standard voice connection – at its peak there were over 600 million such connections in the world
V.34 modems achieve 10 bits/Hz of bandwidth by using high level modulation and DSP
Often though they are forced to operate at lower speeds due to inadequate line SNR
Set-up time is also very long
Dial up networking……..
Now mostly consigned to the history books!

## Slide 9: Crosstalk
A telephone cable usually contains hundreds or thousands of wire pairs packed closely together
Due to the electro-magnetic field created when a signal propagates a signal is induced into the nearby wires.
This is reduced by the
twisting by some crosstalk
still remains
This is a primary limiting
factor for high rate
transmission

## Slide 10: Near-End Crosstalk
Major problem for systems that share the same frequency band upstream and downstream
NEXT

## Slide 11: Far-End Crosstalk
Less severe than NEXT as the FEXT noise is attenuated due to the transmission over the cable length
FEXT

## Slide 12: Co-axial Cable

## Slide 13: Wireline Systems

## Slide 14: ISDN
An ISDN connection provides two 64 kbit/s bearer (B) channels and one 16 kbit/s data (D) channel
Some extra overhead pushes the raw data rate at the customer interface (U-interface) to 192 kbit/s
ISDN uses a 2B1Q (2 data bits are mapped to 4-levels) signal format
This limits the spectrum to about 120 kHz and can typically be supported over an access connection of about 5 km

## Slide 15: Primary rate ISDN access
30 B channels and a 64 kbit/s D channel can be provided at 2.048 Mbit/s in a frame of 125 s duration
TS0 is used for synchronisation and TS16 provides the D channel
The customer is provided with half width 3V pulses on a twisted copper pair coded with HDB3 (or 2.37V pulses on a 75  coaxial cable)
Data is sent in both directions simultaneously using echo-cancelled hybrid (ECH) transmission, and adaptive equalisation

## Slide 16: xDSL technologies
Basic digital subscriber line configuration is to have 2 modems
  one at the customer end and the other in the network
xDSL allows a subscriber line to support both POTS and high speed data
Variants include:
  HDSL - high data rate DSL
  SDSL - single line DSL
  RADSL - rate adaptive DSL
  ADSL - asymmetric DSL
  VDSL - very high rate DSL

## Slide 17: ADSL over POTS Reference Model
DSLAM
ATU-C
CPE
ATU-R
Network
DSLAM - Digital Subscriber Line Access Multiplexer
up to 8 Mbit/s
up to 640 kbit/s
Central Office
Customer Premises
twisted pair
splitter
splitter
PSTN
Switch
Spectrum allocation
4 kHz
POTS
Frequency
1.1 MHz
32 kHz
POTS
UP
DOWN

## Slide 18: DMT Technology
spectrum used
for upstream data
spectrum used
for downstream data
Total bandwidth = 1.1 MHz = 255 Tones
Each tone is QAM modulated and individually optimised with respect to the noise in the channel
Tones may be switched off if the noise is too high
4 kHz
32 kHz
tone spacing
(4.3 kHz)
power
spectrum
1.1 MHz
max 3 dB variation
frequency
POTS

## Slide 19: ADSL key advantages
No cable deployment
  Low installation cost: no civil engineering works are required
  Fast connection of new users
Per-user basis introduction capability
  Investment nearly proportional to service demand
Second virtual line
  line available for telephone calls even when surfing
Always on Connection
  LAN like
  resources used only when data are really transmitted
High peak bitrate
Bitrate scalability from 100 kbit up to 8 Mbit/s

## Slide 20: ADSL Local Loop Impairments
Attenuation
Cross Talk
Unbalanced loops
Noise
Gauge mismatches
Loading coils
Bridged Taps
The performance
of ADSL is
distance dependent

## Slide 21: Loop Qualification
Basic Qualification
  Insulation resistance
  Continuity
  Capacitance
Map Analysis
  Estimation of the insertion loss using maps
Field Testing
  Actual on site testing
  Truck roll
http://www.broadbandspeedchecker.co.uk/
8km
6km
4km
2km

## Slide 22: Emissions from DSL
Emissions from wires carrying DSL have become of increased importance as a number of radio bands overlap the transmission spectrum.

## Slide 23: ADSL Reach
Source: Analysys, IEEE

## Slide 24: ADSL summary
Utilises the legacy copper access network - a major benefit to incumbent telcos
No major upgrades required to the POTS switches
Opens up new revenue streams
Low fixed costs (ADSL rack in exchange etc) but relatively high marginal costs (ADSL modems can cost around $100/pair)
Allows incremental deployment
Very capital efficient in that service is only provided to those who need it
Still not providing true triple play

## Slide 25: VDSL
Broadband services could do with a higher data transfer rate than ADSL can support
The same principles as ADSL (clever DSP) can be applied to address this by limiting the reach of the system
VDSL supports data rates to over 50 Mbit/s to the customer thereby enabling support of these very broadband services
The shorter reach of VDSL though means that data must be carried from the exchange to a point close to the customer (see later)
Bit rate (Mbit/s) | Reach | Suitability
13 | 1.5 km | FTTCab
26 | 1.0 km | FTTC/FTTB
52 | 300 m | FTTB
PCP
Exchange
Existing E-side Cables
Existing D-side Cables
VDSL Cabinet
New Fibre Feed

## Slide 26: Ethernet
Ethernet is a family of frame-based computer networking technologies for local area networks (LANs).
Multiple media options
  Twister Pair Copper
  Coax
  Optical Fibre
Standards for 10Mbit/s, 100Mbit/s (Fast), 1Gbit/s (GE) and recently 10Gbit/s (10GE or XGE).

## Slide 27: Ethernet over twisted pair
Referred to as xBASE-T (where x is 10,100, 1000)
The cables usually used are four-pair twisted pair cable.
Speed (Mbit/s) | Distance (m) | Standard /Year | 
10 | 100 | 10BASE-T 1990 | Four wire (two pair), Cat3 or Cat5, Manchester Coding
100 | 100 | 100BASE-T 1995 | 4B5B coding, Cat5 Cabling using two pair
1000 | 100 | 1000BASE-T 1999 | PAM-5 Coding, recommended Cat5e using four pairs
10000 | 100 | 10GBASE-T 2006 | Shielded or unshielded Cat6, PAM-16

## Slide 28: Cable Types
All contain four twister pairs
Category 3
  Frequencies to 16MHz
Category 5
  Characteristics defined up to 100MHz
Category 5e
  Characteristics defined up to 100MHz
Category 6
  Performance up to 250MHz

## Slide 29: CATV
Originally developed to distribute video to residential communities
Offerings typically include a basic package, a premium package and a pay per view package
The network was designed around a one way broadcast network where filters and scrambling where used to provide conditional access to different customers
Impulse pay per view made use of a telco return channel

## Slide 30: Hybrid Fibre Coax Network
Optical / Electrical Equipment
OLT
Headend
OLT – Optical Line Termination equipment
fibre
coax
Amplifiers
OLT

## Slide 31
CATV Network
There are six main parts to an HFC network
  The headend (Signal reception, origination and modulation point)
  The fibre distribution part (transport from the headend to the remote distribution area)
  The main coaxial distribution (tree) cable
  Distribution coaxial (branch) cable including distribution taps
  The drop cable to the home and in house wiring
  Customer premises equipment

## Slide 32
CATV
The most important characteristic of Hybrid Coax networks (HFC) is their ability to allow a customer to use his TV directly for all unscrambled channels
The characteristic impedance of coaxial cable used in CATV is 75 ohms
The well known principles of transmission line theory apply fully to CATV technology
Coaxial cable attenuation is a function
  Diameter
  Temperature
  Dielectric construction
  Frequency
  Requires equalisation in amplifiers

## Slide 33
A typical CATV Frequency Plan
*Note that channels are not consecutive
**The cable converter has a high quality broadband tuner and output circuitry that puts the desired channel on a low
Band channel not occupied in the local off the air spectrum (Typically 2,3,4). The TV or VCR is tuned to this channel
And behaves like a monitor

## Slide 34
CATV channel carrying capacity

## Slide 35
CATV Network
The fibre part transports the signal to the neighbourhood using Sub carrier multiplexing techniques. This part terminates in an Optical Network Unit
A coaxial tree branch distribution system then feeds the neighbourhood. Line extenders are required every approx. 300m. depending on the bandwidth of the system
Since the distribution portion of the plant is operated at higher power levels, non linear effects become important. The maximum number of amplifiers that can be placed in cascade is therefore limited by the build up of noise and distortion
Non linear distortion is measured by the Composite Triple Beat parameter, which is a measure of the interference generated by all the carriers beating together.

## Slide 36
CATV signal quality
The principal picture impairments can be divided in to two categories:-
  Non coherent noise arising from random noise such as thermal noise. This gives rise to a snowy picture
  Coherent noise arising from
    the ingress of video signals in to the cable network,
    reflections of the signal from transmission line discontinuities
    Cross modulation of the video giving rise to beats (horizontal lines moving through the picture)
An experienced cable network designer must balance noise, non linear distortions and cost to find an optimum solution.
Starting at the home the objective is to deliver at least 0dBm to the TV. A weaker signal produces snowy pictures and a stronger one overloads the TV tuner resulting in cross modulation of the channels

## Slide 37
DOCSIS 1.0
Data Over Cable Service Interface Specifications (DOCSIS) DOCSIS 1.0 completed in March 1997 – A family of specifications
The main objective is to provide a transparent high speed link to the Internet. It requires that the HFC network is two way

## Slide 38
DOCSIS

## Slide 39
DOCSIS 1.1 & 2.0
Data Over Cable Service Interface Specifications (DOCSIS) DOCSIS 1.1 was completed in March 1999
Enhanced DOCSIS 1.0 services by addressing :-
  Quality of Service
  IP multicast
  Security
  Operational Support
DOCSIS 1.1 included methods to guarantee QOS to different services going through the same cable modem or on the same RF channels
  Packet Classification
  Service Flows – which define specific guarantees and limits of types of traffic
  Dynamic service assignment – allows the system to dynamically create and delete service flows
DOCSIS 2.0 increased the upstream of DOCSIS 1.1 x3 and improved the robustness against interference by the use of A-TDMA and S-CDMA

## Slide 40
EuroDOCSIS
The DOCSIS specification has been adapted for use on the networks of European CATV operators. This adapted European version has been called EuroDOCSIS.
The main differences are in
  The modulation format (where ITU-T J.83 Annex A is used)
  A different frequency split to separate the upstream and the downstream directions
  Different Management Information Bases (MIBs)

## Slide 41
DOCSIS Protocol Stack
Physical Media Dependent Layer (PMD)
Data Link Encryption
MAC
MPEG-2 Transport
(Downstream Only)
Internet Protocol (IP)
Logical Link Control (LLC)
Physical
Data Link
Layer

## Slide 42
DOCSIS Protocol Stack
The upstream PMD sublayer uses a FDMA/TDMA burst access mechanism. Two modulation formats are used QPSK and 16QAM with 5 symbol rates. The lowest symbol rate is 160ksymbols/s and the highest 2.56Msymbols/s. Reed Solomon FEC correct burst errors.
The downstream transmission format is based on the ITU-T J.83 Annex B standard for digital video transmission on cable systems. It uses a 6MHz, 64/256 QAM modulation format. A concatenated coding scheme is also used.
The MPEG-2 transport sublayer is used to provide a common platform for the transfer of video and data on the HFC network
The MAC layer is essential for DOCSIS operation on the shared HFC network. On the downstream the cable modems listen to all the traffic flow from the CMTS and accept messages targeted to them.
In the upstream direction a FDMA/TDMA Multiple access scheme is implemented. A cable modem first requests bandwidth authorisation from the CMTS, listens to the downstream bandwidth allocation message and then transmits if allowed to do so.

## Slide 43: DOCSIS 3.0 Features
MAC Layer
  Downstream Channel Bonding
  Upstream Channel Bonding
Network Layer
  IPv6 support
  IP Multicast (IGMPv3/MLDv2, SSM, QoS)
Security
  Certificate Revocation Management
  Runtime SW / Config validation
  Enhanced Traffic Encryption (AES)
  Certificate Convergence
  Early Authentication & Encryption
  TFTP Proxy
Network Management
  Diagnostic Log (Flaplist)
  Extension of Internet Protocol Data Records (IPDR) usage
  Capacity management
  Enhanced signal quality monitoring
Physical Layer
  Switch-able 5-42 MHz, 5-65 MHz, or 5-85 MHz US band
  S-CDMA active code selection with new Logical channel
Commercial Services
  T1/E1 Circuit Emulation support

## Slide 44: Downstream Bonding Service Drivers
Packet bonding of a minimum of 4 channels
  Delivers in excess of 150 Mbps
  Seamless migration from DOCSIS 1.x/2.0
IP Video over DOCSIS(VDOC)
  High definition Video to multiple devices
  High BW Internet streaming
Video conferencing
  TelePresence
Commercial service
  High BW data services
  Bonded T1
  High BW Ethernet/L2VPN service

## Slide 45: DOCSIS 3.0 Channel Bonding
6 MHz
6 MHz
6 MHz
6 MHz
38 Mbps
38 Mbps
38 Mbps
38 Mbps
152 Mbps
Logical Channel Bonding Technology
DOCSIS 3.0 is the next generation of the DOCSIS standard
DOCSIS 2.0 is limited to single channel’s capacity
DOCSIS 3.0 employs packet bonding across multiple channels
  Initially will bond 4 channels
  8 channel-capable silicon coming soon
  Upstream bonding in 2010
  Increased speeds 100Mbps+
Notes: 45

## Slide 46: Further Developments
Traffic “Grooming”
MPEG-4
Broadcast to narrowcast QAM injection
  Reduce broadcast domains to smaller DOCSIS & video service groups
  Ultimately a complete Unicast lineup on a per node basis
Analog reclamation for more digital spectrum
  More QAM channels for Digital Broadcast, VoD, Switched Digital Video (SDV) and DOCSIS
Use every channel available
  Manage the channel lineup, fill in the gaps, mitigate noise to enable all spectrum
1GHz upgrade
  Make new spectrum for new CPE above 860 MHz

## Slide 47: 1 GHz Upgrade
Network Impact
  <= 750 MHz of BW may not be enough
  Node splitting & SDV alone do not solve HFC BW problem
  1 GHz BW upgrade required
1GHz Network Benefits
  Value added capacity
    60 analog 6 MHz chs gained
    Minimal cost per home passed cost to implement
    Electronic-only drop-ins in most cases
1 GHz is a cost-effective tool to increase broadcast and narrowcast BW

## Slide 48: Why DOCSIS 3.0
DOCSIS 3.0 - channel bonding for higher capacity
  Enable faster HSD service
  MxN mac domains now
  Enable video over IP solutions
M-CMTS (Modular Cable Modem Termination System)
  Lower cost downstream PHY
  De-couple DS and US ports
I-CMTS (Integrated Cable Modem Termination System)
  Allows higher capacity in same box
  Same wiring
Notes: New technologies are being pursued to address the DS bottleneck conundrum.
DOCSIS 3.0 uses a channel bonding technique to achieve higher capacity links, enable faster high speed data (HSD) service, and provide M x N MAC domains to enable video over IP solutions.
The idea of multiple grants per request or outstanding requests with DOCSIS 3.0 is also a good idea for US speed, but still doesn't fix the CPU issue on the CM.
The modular CMTS (M-CMTS) architecture is promoted to achieve better DOCSIS economics, lower cost DS PHY, and de-couple DS and US ports. One day we may see fiber optic nodes with DOCSIS physical layer chips embedded so we can use ingress cancellation at the node, digital links from the node back to the headend without the need to amplify, and no more laser clipping. Of course, this means all traffic needs to be DOCSIS-based on the US!
The integrated-CMTS idea is a way to use “off-the-shelf” external QAM boxes and the existing CMTS just for US connectivity. This allows return on invest and no “fork-lift” upgrades of the CMST chassis and/or limited cabling changes.

## Slide 49: DOCSIS 3.0/M-CMTS:Remarks
Promises ten times BW at fraction of cost
Introduce new High Speed Data service of 50 to 75 Mbps
Widespread deployment of DS Bonding in 2008
Backward compatible with existing DOCSIS standards
Allows migration of existing customers to higher tier and DOCSIS 3.0 capability
Allows more BW for legacy DOCSIS 2.0 CM
Allows for a phased deployment
IPV6, US bonding, and other features will follow

## Slide 50: Powerline Communications
The electrical distribution lines can be used to distribute data
A number of systems such as HomePlug allow users to set up LANs over their existing in-home wiring
Broadband delivery over powerlines is also possible

## Slide 51: Broadband over Powerline
Variations in the way that power is transported between countries (predominantly EU vs US) has led to a lack of standardisation
Widespread concerns over interference with radio

## Slide 52: IEEE P1901
Draft released in Jan 2010, Release Sept 2010
Two different PHY layers, one based on OFDM modulation (following HomePlug) and another based on Wavelet modulation
Uses forward error correction based on convolutional turbo codes

## Slide 53: Conclusions
Still a lot of work for copper to do
For low cost networking copper still dominates
Price of the copper itself has risen sharply in recent years, making fibre more attractive in some installs