## Slide 1: Multimedia Systems
Dr Laura Toni
l.toni@ucl.ac.uk
University College London

## Slide 2: Today Lecture
Introduction to Information compression
  Source Coding
  Information and Entropy
  Variable length coding
  Quantization
Multimedia Systems
  Image and Lossy Compression
    Transforms
    JPEG Quantization
    JPEG Lossless Compression
  Video Compression
    Motion Compensation

## Slide 3: Compressing Digital Video
Exploit temporal redundancy between frames
  Only the sun has changed position between these 2 frames
Exploit spatial redundancy within frames (like JPEG: transform, quantize, Variable Length Coding)
Previous Frame
Current Frame

## Slide 4: Difference Frames
Differences between two frames can be caused by
  Camera motion: the outlines of background or stationary objects can be seen in the Diff Image
  Object motion: the outlines of moving objects can be seen in the Diff Image
  Illumination changes (sun rising, headlights, etc.)
  Noise
  Scene cuts
This difference might still have some correlation – we want to remove it with compression

## Slide 5: Types of Motion: Translation
Translational motion: simple movement of typically rigid objects
Camera pans vs. movement of objects
Frame n
Frame n+1

## Slide 6: Types of Motion: Rotation & Zoom
Rotation: spinning about an axis
  Camera versus object rotation
Zooms – zoom in, zoom out
  Camera zoom vs. object zoom (movement in and out)
Frame n+1 (Rotation)
Frame n+2 (Zoom)
Frame n

## Slide 7: Motion Estimation
For some portion of the frame, estimate its movement between 2 frames- the current frame and the reference frame
What is some portion?
  Individual pixels (all of them)?
  Lines/edges (have to find them first)
  Objects (must define them)
  Uniform regions (just chop up the frame)

## Slide 8: Motion Vectors
A motion vector (MV) describes the offset between the location of the block being coded (in the current frame) and the location of the best-match block in the reference frame
T=1 (reference)
T=2 (current)

## Slide 9: Motion Compensation
This glued together frame is called the motion compensated frame
The encoder can also form the difference between the motion compensated frame and the actual frame.
This is called the motion compensated difference frame
This difference frame formed using MC should have less correlation between pixels than the difference frame formed without using MC

## Slide 10: Motion compensated difference frames
E1 & E2 called prediction error or difference frames
Do we prefer to compress and send E1 or MV+E2 ?
Reference Frame F(n-1)
Original Frame F(n)
Difference Image E1=F(n)-F(n-1)
Motion compensated frame M(n)
Motion compensated difference image E2=F(n) – M(n)

## Slide 11: Motion estimation philosophy
Most of the time, for a given representation quality
  fewer bits to send MV+E2 instead of sending E1
  fewer bits to send E1 instead of sending F itself.

## Slide 12: Reference Frame
0 1 2 3

## Slide 13: Temporal Location of Reference

## Slide 14: Thank You

## Slide 15: Today Lecture
Introduction to Information compression
  Source Coding
  Information and Entropy
  Variable length coding
  Quantization
Multimedia Systems
  Image and Lossy Compression
    Transforms
    JPEG Quantization
    JPEG Lossless Compression
  Video Compression
    Motion Compensation

## Slide 16: MPEG Frame Types
Intra (I) pictures: coded by themselves, as still images. No temporal coding. No motion vectors.

## Slide 17: MPEG Frame Types
Forward Motion Compensated predicted (P) pictures – forward motion compensated from the previous I or P frame

## Slide 18: MPEG Frame Types
Motion Compensated interpolated (B) pictures – forward, backward, and interpolatively motion compensated from previous/next I/P frames

## Slide 19
I-P-B Structure - example
Graphical example that shows how in P and B frames we actually only compress the “difference” with respect to one (or more) reference frame

## Slide 20
I-P-B Structure - example

## Slide 21: History of Video Compression Standards
MPEG-1
MPEG-2
MPEG-4
HEVC
1/25
1/50
1/100
Compression ratio
time
1991
1994
2003
2013
DVD
Digital TV
Video Streaming
HD DVD
Full-HD mobile broadcasting
Ultra- HD (4K/8K) broadcasting
Video CD
VideoConference

## Slide 22: Competing Codecs
VP8/VP9,
AV1
MPEG/ITU HEVC/H.265
use scalar or vector quantization
use temporal compression
highly asymmetric
4K full-HD videos
Compression up to 50% compared to previous codecs

## Slide 23: Competing Codecs
VP8/VP9,
AV1
MPEG/ITU HEVC/H.265

## Slide 24: Performance comparison
“Rate-distortion performance of contemporary video codecs: Comparison of Google/WebM VP8, AVC/H. 264, and HEVC TMuC”, E Ohwovoriole and Y Andreopoulos - LENS Symp., London, 2010.
http://www.ee.ucl.ac.uk/~iandreop/OHWOVORIOLE_LCS_2010_H264_VP8_HEVC_comparison.pdf

## Slide 25: Raw Bandwidth
Resolution (WxL) | 24bit@25fps | 8bit@25fps | 8bit@15fps | 8bit@5fps
4K (3840x2160) | 5 Gbit/s | 1.6 Gbit/s | 995 Mbit/s | 331 Mbit/s
HDTV (1920x1080) | 1.3 Gbit/s | 414 Mbit/s | 248 Mbit/s | 83 Mbit/s
VGA (640x480) | 184 Mbit/s | 61 Mbit/s | 36 Mbit/s | 12 Mbit/s
SCIF (704x576) | 240 Mbit/s | 80 Mbit/s | 48 Mbit/s | 16 Mbit/s
CIF (352x288) | 60 Mbit/s | 60 Mbit/s | 12 Mbit/s | 4 Mbit/s
QCIF (176x144) | 12 Mbit/s | 12 Mbit/s | 3 Mbit/s | 1 Mbit/s
Uncompressed video is BIG
A DVD would hold max 5 secs of uncompressed video at 1920x1080 resolution
6 MHz channel for transmission therefore maximum possible bitrate is 18 Mb/sec
Requires compression of 83:1
Raw Bandwidth = color depths * W * L * refresh frequency

## Slide 26: Future Video Applications
Immersive Communications (holoportation, from Microsoft)
Virtual Reality, 360 Videos
Telepresence
(from Cisco)

## Slide 27: Speech/Audio/Video Coding Summary
Requirements for Coding of each Source
Speech Coding Principle
Discontinuous Transmission
GSM Speech Coding
  RPE-LPC
  Enhanced Full Rate
Different Video Coding Formats, motion compensation

## Slide 28: Web References
3G Latest
http://www.umts-forum.org/
GSM Information
http://www.gsmworld.com/
Fraunhofer Full-HD Voice
http://www.full-hd-voice.com/
MPEG Information
http://www.chiariglione.org/mpeg/
Speech Coding
http://www-mobile.ecs.soton.ac.uk/speech_codecs/
Netflix TechBlog
http://techblog.netflix.com/search/label/encoding